## Slide 1: Pensinyalan (2)
Perbandingan antara sinyal analog dan digital

## Slide 2
3.4 Analog versus Digital
Low-pass versus Band-pass
Digital Transmission
Analog Transmission

## Slide 3
Figure 3.19 Low-pass and band-pass

## Slide 4
The analog bandwidth of a medium is expressed in hertz; the digital bandwidth, in bits per second.
Note:

## Slide 5
Digital transmission needs a low-pass channel.
Note:

## Slide 6
Analog transmission can use a band-pass channel.

## Slide 7
3.5 Data Rate Limit
Noiseless Channel: Nyquist Bit Rate
Noisy Channel: Shannon Capacity
Using Both Limits

## Slide 8
Example 7
Consider a noiseless channel with a bandwidth of 3000 Hz transmitting a signal with two signal levels. The maximum bit rate can be calculated as
Bit Rate = 2  3000  log2 2 = 6000 bps

## Slide 9
Example 8
Consider the same noiseless channel, transmitting a signal with four signal levels (for each level, we send two bits). The maximum bit rate can be calculated as:
Bit Rate = 2 x 3000 x log2 4 = 12,000 bps

## Slide 10
Example 9
Consider an extremely noisy channel in which the value of the signal-to-noise ratio is almost zero. In other words, the noise is so strong that the signal is faint. For this channel the capacity is calculated as
C = B log2 (1 + SNR) = B log2 (1 + 0) = B log2 (1) = B  0 = 0

## Slide 11
Example 10
We can calculate the theoretical highest bit rate of a regular telephone line. A telephone line normally has a bandwidth of 3000 Hz (300 Hz to 3300 Hz). The signal-to-noise ratio is usually 3162. For this channel the capacity is calculated as
C = B log2 (1 + SNR) = 3000 log2 (1 + 3162) = 3000 log2 (3163)
C = 3000  11.62 = 34,860 bps

## Slide 12
Example 11
We have a channel with a 1 MHz bandwidth. The SNR for this channel is 63; what is the appropriate bit rate and signal level?
Solution
C = B log2 (1 + SNR) = 106 log2 (1 + 63) = 106 log2 (64) = 6 Mbps
Then we use the Nyquist formula to find the
number of signal levels.
4 Mbps = 2  1 MHz  log2 L  L = 4
First, we use the Shannon formula to find our upper limit.

## Slide 13
3.6 Transmission Impairment
Attenuation
Distortion
Noise

## Slide 14
Figure 3.20 Impairment types

## Slide 15
Figure 3.21 Attenuation

## Slide 16
Example 12
Imagine a signal travels through a transmission medium and its power is reduced to half. This means that P2 = 1/2 P1. In this case, the attenuation (loss of power) can be calculated as
Solution
10 log10 (P2/P1) = 10 log10 (0.5P1/P1) = 10 log10 (0.5) = 10(–0.3) = –3 dB

## Slide 17
Example 13
Imagine a signal travels through an amplifier and its power is increased ten times. This means that P2 = 10 ¥ P1. In this case, the amplification (gain of power) can be calculated as
10 log10 (P2/P1) = 10 log10 (10P1/P1)
= 10 log10 (10) = 10 (1) = 10 dB

## Slide 18
Example 14
One reason that engineers use the decibel to measure the changes in the strength of a signal is that decibel numbers can be added (or subtracted) when we are talking about several points instead of just two (cascading). In Figure 3.22 a signal travels a long distance from point 1 to point 4. The signal is attenuated by the time it reaches point 2. Between points 2 and 3, the signal is amplified. Again, between points 3 and 4, the signal is attenuated. We can find the resultant decibel for the signal just by adding the decibel measurements between each set of points.

## Slide 19
Figure 3.22 Example 14
dB = –3 + 7 – 3 = +1

## Slide 20
Figure 3.23 Distortion

## Slide 21
Figure 3.24 Noise

## Slide 22
3.7 More About Signals
Throughput
Propagation Speed
Propagation Time
Wavelength

## Slide 23
Figure 3.25 Throughput

## Slide 24
Figure 3.26 Propagation time

## Slide 25
Figure 3.27 Wavelength